inter-american convention against the	OEA/Ser.L/XXII.2.14

illicit manufacturing of and trafficking	CIFTA/CC-XIV/doc.11/13

in firearms, ammunition, explosives, and	19 April 2013

OTHER RELATED MATERIALS (CIFTA)	Original: English

### Consultative Committee

Fourteenth Regular Meeting

April 25, 2013

Washington, D.C.

DRAFT

OAS FIREARMS STANDARDS

MARKING AND RECORDKEEPING

(Prepared by the CIFTA Technical Secretariat)

Table of Contents

Introduction	1

Marking and Recordkeeping	2

Scope	2

Normative Reference	2

Terms and definitions	2

1. Firearms Marking	2

1.1 Marking at the time of manufacture	3

1.1.1 Content	3

1.1.2 Form	3

1.1.3	Location	3

1.1.4	Physical characteristics	4

1.1.5	Method	4

1.2 Marking at the time of import	4

1.2.1 Content	4

1.2.2 Form	5

1.2.3  Location	5

1.2.4 Physical characteristics	5

1.2.5 Method	6

1.2.6 Exceptions	6

1.3 Marking at the time of confiscation or forfeiture	6

1.3.1 Content	6

1.3.2 Form	7

1.3.3 Location	7

1.3.4 Physical characteristics	7

1.3.5 Method	8

1.4 Other suitable markings	8

1.4.1 National Entity	8

2. Recordkeeping	8

2.1	General	8

2.2	Records to be kept	9

2.3	Keeper(s) of the records	10

2.4	Method of recordkeeping	10

2.5	Access to records	10

Appendix A	12

# Introduction

The Inter-American Convention against the Illicit Manufacturing of and Trafficking in Firearms, Ammunition, Explosives, and Other Related Materials (CIFTA) was adopted in 1997 as a regional instrument to prevent, combat and eradicate the illicit manufacturing of and trafficking in firearms, ammunition, explosives and other related materials and to promote and facilitate cooperation and exchange of information and experiences in this regard. CIFTA is a legally binding instrument that contains a series of provisions to be implemented by the States Parties in order to strengthen their legal framework in this area.

Article VI of the CIFTA regulates the marking of firearms. The Convention stipulates that for the purpose of identification and tracing of firearms, States Parties shall require appropriate markings at the time of: a) manufacture; b) import; and c) confiscation or forfeiture (for weapons to be retained for official use). CIFTA, in its Article XI, also requires that States Parties keep the necessary information to trace and identify illicitly manufactured or trafficked firearms.

To help facilitate the implementation of these provisions, the OAS Member States approved in 2007 the OAS Model Legislation on the Marking and Tracing of Firearms. This Model Legislation contains a series of suggested provisions that Member States should adopt, in accordance with their legal systems, fundamental laws and policies, to strengthen their legislative regimes in the area of marking and tracing.

The marking of firearms is a crucial step in combating the illicit trafficking in firearms because firearms are more easily traceable and can therefore be more effectively linked to crimes in which they were used, thereby increasing law enforcement and prosecutorial capabilities. Effective tracing operations depend greatly on the effective recordkeeping of firearms information.

To complement the provisions of both the Convention and its Model Legislation and facilitate their practical implementation, the CIFTA Technical Secretariat is pleased to present draft OAS Firearms Standards on Marking and Recordkeeping that build upon standards, best practices and guidelines that have been prepared and implemented at the international, regional and sub-regional levels. This document was drafted in collaboration with the United Nations Coordinating Action on Small Arms (CASA) mechanism so as to be compatible with International Small Arms Control Standards (ISACS).

# Marking and Recordkeeping

## Scope

This document provides practical guidance on adequate firearms marking and recordkeeping practices at the time of: a) manufacture; b) import; and c) confiscation or forfeiture – for weapons to be retained for official use.

## Normative Reference

- The Inter-American Convention against the Illicit Manufacturing of and Trafficking in Firearms, Ammunition, Explosives, and Other Related Materials (CIFTA).

- OAS Model Legislation on the Marking and Tracing of Firearms.

- OAS Model Legislation and Commentaries on Recordkeeping, Confidentiality, and Exchange of Information Regarding the Manufacturing of and Trafficking In Firearms, Ammunition, Explosives, and Other Related Materials (PENDING APPROVAL)

- International Small Arms Control Standards (ISACS).

- ISO 3166-1, Codes for the representation of names of countries and their subdivisions – Part 2: Country Codes

## Terms and definitions

For the purposes of this document, the words 'shall', 'should', 'may' and 'can' are used to express provisions in accordance with their usage in International Organization for Standardization (ISO) standards.

a) “shall” indicates a requirement. It is used to indicate requirements strictly to be followed in order to conform to the document and from which no deviation is permitted.

b) “should” indicates a recommendation. It is used to indicate that among several possibilities one is recommended as particularly suitable, without mentioning or excluding others, or that a certain course of action is preferred but not necessarily required, or that (in the negative form, 'should not') a certain possibility or course of action is deprecated but not prohibited.

c) “may” indicates permission. It is used to indicate a course of action permissible within the limits of the document.

d) “can” indicates possibility and capability. It is used for statements of possibility and capability, whether material, physical or causal.

### 1. Firearms Marking

All firearms shall be marked at the time of their:

1.1 Manufacture

1.2 Import

1.3 Confiscation by or forfeiture to the State (if retained by the State for official use)

Since illicit firearms can be assembled from legally manufactured parts and components that have been illicitly trafficked, parts and components that are essential to the operation of a firearm should also be marked in accordance with 1.1, 1.2 and 1.3.

#### 1.1 Marking at the time of manufacture

##### 1.1.1 Content

All firearms shall have applied to them, at the time of their manufacture, markings containing at least the following information:

- Country of manufacture (or 2 digit ISO country code)

- Name of manufacturer (or code)

- Serial number unique to the:

  - Manufacturer; or

  - Type/model of the firearm produced by the manufacturer

The following additional markings should also be placed upon the firearm at the time of its manufacture in order to further identify it for tracing purposes:

- Year of manufacture

- Type or model

- Caliber

##### 1.1.2 Form

Markings shall be expressed alphanumerically, as follows:

| XX | - | XXXX | - | 99 | - | 99 | - | 99999 | - | 99 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Country of Manufacture (2 digit ISO Country code) |  | Manufacturer’s Name (or code) |  | Year of manufacture (2 numbers) |  | Type/Model |  | Serial number |  | Caliber |

##### Location

Required markings shall be placed on the most essential part of a firearm: frame or receiver.

When possible, markings should additionally be applied to other pressure-bearing parts and components of the firearm, including: Barrel, Slide, cylinder or bolt

Note: The application of such additional marks can assist in the identification, recordkeeping and tracing of illicit firearms that have been assembled from the parts and components of a number of different weapons and whose frame or receiver is unmarked or has had its markings removed; as well as illicit shipments of parts and components of firearms.

For weapons with frames made of non-metallic material (e.g. polymers), the marking shall be applied to a metal plate permanently embedded in the material of the frame in such a way that:

- the plate cannot easily or readily be removed

- removing the plate would destroy a portion of the frame

When marked, the steel plate should contain enough empty space to receive at least one import marking of the same character size (see Clause 1.2).

##### Physical characteristics

Markings shall be applied to an exposed surface of the firearm and shall be:

- legible

- conspicuous without technical aids or tools

- durable (resistant throughout the expected lifetime of the firearms to normal operational wear and tear)

- not easily susceptible to being obliterated, altered or removed

- recoverable (as far as technically possible)

##### Method

The stamping method should be used to apply markings to firearms at the time of manufacture. Markings shall have a depth of at least 0.2mm

#### 1.2 Marking at the time of import

Note: Although the obligation to require appropriate marking on imported firearms is on the importing state, the importing state may by contract or other means require that import markings be placed upon the firearms by the manufacturer of the country of export. Applying such marks at the time of manufacture is advised because it avoids the need to re-mark the firearms at time of import.

##### 1.2.1 Content

Imported firearms that already possess markings in accordance with Clause 1.1 shall have applied to them at the time of import additional marking identifying:

a) Country of import

b) Importer’s name (or code)

c) Year of import

Imported firearms that do not possess markings in accordance with Clause 1.1 shall have applied to them additionally at the time of import a serial number unique to a) and c) above.

##### 1.2.2 Form

Markings shall be expressed alphanumerically, as follows:

| XX | - | XXX | - | 99 | - | 99999 |
| --- | --- | --- | --- | --- | --- | --- |
| Country of import (2- digit ISO country code) |  | Importer’s name or code |  | Year of import (2 numbers) |  | Serial number (if the firearm does not possess one) |

##### 1.2.3  Location

Required import markings shall be placed on the most essential part of a firearm (frame or receiver) and, in addition, may be applied to other pressure-bearing parts (barrel, slide, cylinder, bolt or breech block). For more details, please refer to Clause 1.1.3

Import markings should be applied adjacent to the existing marks but should be visibly distinguishable from them.

For weapons with frames made of non-metallic materials (e.g. polymers), the import mark should be applied on the embedded steel plate containing the main marking (see Clause 1.1.3). If not possible, the import marking may be applied directly to the non-metallic frame.

When an import marking is applied directly to a non-metallic frame:

a)	It should be applied to a part of the frame that is least likely to suffer from wear and tear during the course of normal operational use; and

b)	The same import marking should also be applied to at least one essential metallic component of the weapon (e.g. barrel, slide, cylinder or bolt).

##### 1.2.4 Physical characteristics

Import markings shall be applied to and exposed surface of the firearm and shall be:

- legible

- conspicuous without technical aids or tools

- durable (resistant throughout the expected lifetime of the firearms, to normal operation and tear)

- not easily susceptible of being obliterated, altered or removed

- recoverable (as far as technically possible)

##### 1.2.5 Method

If import markings are applied at the time of manufacture, marking techniques stipulated in Clause 1.1.5 should be used to apply them.

If import markings are applied at the time of import, the pin stamping method should be used to apply markings. Other methods may also be applied (this includes mechanical or laser engraving).

Import marking should have a depth of at least:

- 0.1 mm when applied to metal

- 0.2 mm when applied to non-metallic materials (e.g. polymers)

##### 1.2.6 Exceptions

Import markings need not be applied to:

- firearms imported temporarily for verifiable, lawful purposes

- firearms that have been duly marked and that have been temporarily exported from and re-imported into the same country for verifiable lawful purposes

#### 1.3 Marking at the time of confiscation or forfeiture

##### 1.3.1 Content

Confiscated or forfeited firearms that are not to be destroyed, but retained for official use, if not already marked according to Clause 1.1 and 1.2, shall have applied to them markings identifying the:

- country of confiscation

- year of confiscation

- serial number unique to a) and b) – if the firearm does not already have a serial number.

If the firearms already possess marking in accordance with Clause 1.1 and 1.2, no additional markings need to be applied at the time of confiscation.

##### 1.3.2 Form

Confiscation/forfeiture markings shall be expressed alphanumerically, as follows:

| XX | - | 99 | - | 99999 |
| --- | --- | --- | --- | --- |
| Country of confiscation (2 digit ISO country code) |  | Year of confiscation (2 numbers) |  | Serial number (if the firearm does not possess one) |

##### 1.3.3 Location

Required confiscation/forfeiture markings shall be applied to the most essential part of a firearm (frame or receiver) and, in addition, may be applied to other essential parts (barrel, slide, cylinder, bolt or breech block). For more details, please refer to Clause 1.1.3

Markings should be applied adjacent to the existing marks but should be visibly distinguishable from them.

For weapons with frames made of non-metallic materials (e.g. polymers), the corresponding mark should be applied on the embedded steel plate containing the main marking (see Clause 1.1.3) If not possible, the confiscation marking may be applied directly to the non-metallic frame.

When a marking is applied directly to a non-metallic frame:

a)	 It should be applied to a part of the frame that is least likely to suffer from wear and tear during the course of normal operational use; and

b)	 The same confiscation marking should also be applied to at least one essential metallic component of the weapon (e.g. barrel, slide, cylinder, bolt, or breech block).

##### 1.3.4 Physical characteristics

Markings shall be applied to and exposed surface of the firearm and shall be:

a)	legibly

b)	conspicuous without technical aids or tools

c)	durable (resistant throughout the expected lifetime of the firearms, to normal operation and tear)

d)	not easily susceptible of being obliterated, altered or removed

e)	recoverable (as far as technically possible)

##### 1.3.5 Method

The pin stamping method should be used to apply markings at this time. Other methods may also be applied (this includes mechanical or laser engraving).

Markings should have a depth of at least:

- 0.1 mm when applied to metal

- 0.2 mm when applied to non-metallic materials (e.g. polymers)

#### 1.4 Other suitable markings

##### 1.4.1 National Entity

If the firearm will be assigned to a national entity (e.g. Police or Military), it may be marked with a code identifying the corresponding entity. The mark should be placed, when possible, adjacent to the existing marks on the frame or receiver of the weapon but should be visually distinguishable from the other markings.

## 2. Recordkeeping

PENDING UPON APPROVAL OF THE DRAFT MODEL LEGISLATION AND COMMENTARIES ON RECORDKEEPING, CONFIDENTIALITY, AND EXCHANGE OF INFORMATION REGARDING THE MANUFACTURING OF AND TRAFFICKING IN FIREARMS, AMMUNITION, EXPLOSIVES, AND OTHER RELATED MATERIALS.

### General

Information necessary to trace and identify firearms shall be kept and maintained for a reasonable time by the competent national authority.

To the extent possible, firearms records should be kept indefinitely. Records relating to the manufacturing of firearms should be kept for at least 30 years and all other records should be kept for at least 20 years.

For the purposes of recordkeeping, the markings on the frame or receiver shall be the main reference point for identifying a weapon. If the frame or receiver of a weapon to be recorded is not marked, markings that appear on other essential components of the weapon (e.g. barrel, slide, cylinder or bolt) shall be recorded, along with an indication of the part on which the markings appear.

Note: firearms, particularly older models, can bear numbers, in addition to serial numbers, that are not unique (e.g. assembly numbers, patent numbers and patent use numbers). Care should be taken to distinguish these non-unique numbers from unique serial numbers when recording the details of a weapon.

### Records to be kept

For each individual firearm, the recorded information shall include – at a minimum –the following, where applicable in each instance:

- country of manufacture;

- name of manufacturer;

- serial number;

- year of manufacture;

- weapon type/model;

- caliber;

- The name and location (address) of the owner and legal user of a firearm and each subsequent owner and legal user, until the firearm leaves the jurisdiction of the State;

- The date of entry of the corresponding information on the records;

- Location of markings on the firearm (e.g. on the frame/receiver, barrel, slide, etc);

Additionally, for exported firearms:

- Export authorization number (designated by the exporting State);

- Import authorization number (designated by the importing State);

- In-transit authorization number (designated by the in-transit State);

- Identification of the in-transit country;

- The issuance and expiration dates of the import, export and in-transit licenses authorizations;

- Point of departure in the country of export;

- Date of export;

- Owner of the firearm prior to export;

- Country to which the firearms have been exported;

- Identification of the final recipient;

- Identification of the end-user;

- End-user certificate;

- Broker information;

- Information on the shippers.

- Arrival point in the country of import;

- Date of delivery;

- Classification, description and quantity of the shipment;

For imported weapons:

- Export authorization number (designated by the exporting State);

- Import authorization number (designated by the importing State);

- In-transit authorization number (designated by the in-transit State);

- Identification of the in-transit country;

- The issuance and expiration dates of the import, export and in-transit licenses authorizations;

- Importer’s name;

- Date of import (day, month and year);

- Country from which the weapon has been imported;

- Point of departure in the country of export;

- Owner of the firearm prior to export;

- Identification of the final recipient;

- Identification of the end-user;

- End-user certificate;

- Broker information;

- Information on the shippers;

For confiscated firearms not destined for destruction:

- Date of confiscation;

- Confiscating entity;

- Grounds for confiscation;

- When applicable, confiscation serial number (see Clause 1.3);

- Official use to which the firearms are being put;

For weapons destined for destruction:

- Date of destruction;

- Method of destruction;

- Entity that carried out the destruction;

- Destruction verification certificate number.

Note:  The entity that verifies the destruction shall be different from and independent of the entity that carries out the destruction.

Additionally, states shall keep record of the following:

  - The names, addresses and contact details of authorized producers, dealers, importers, exporters and, brokers of firearms.

  - Records pertaining to firearms held by companies that go out of business.

### Keeper(s) of the records

The above records of all firearms under the jurisdiction of a State should be maintained in a centralized database administered by a competent State authority.

Should it not be possible to maintain records in a centralized manner, records may be maintained in a decentralized manner, e.g. by administrative sub-units of the State and/or by relevant nongovernmental actors including manufacturers, wholesalers, retailers, brokers, transport agents, etc.

Regardless of whether records are maintained in a centralized or in a decentralized manner, they shall be accessible to competent State authorities in accordance with Clause 2.5

### Method of recordkeeping

Records should be maintained in electronic format.

Records should be backed up regularly to prevent data loss.

### Access to records

Competent State authorities, including the Single Operational Points of Contact for the Tracing of Firearms, should have full access to all records relating to firearms held under the jurisdiction of the State, regardless of whether they are maintained in a centralized or in a decentralized manner.

The holders of records relating to firearms, regardless of whether they are governmental or non-governmental entities, shall provide timely responses to requests for information submitted by competent State authorities.

Records shall be maintained in such a manner that allows for accurate and comprehensive information related to the history of a firearm to be retrieved from them within one week of a request being received from a competent State authority.

# Appendix A

ISO 3166-1-alpha-2 code

| AF | AFGHANISTAN |
| --- | --- |
| AX | ÅLAND ISLANDS |
| AL | ALBANIA |
| DZ | ALGERIA |
| AS | AMERICAN SAMOA |
| AD | ANDORRA |
| AO | ANGOLA |
| AI | ANGUILLA |
| AQ | ANTARCTICA |
| AG | ANTIGUA AND BARBUDA |
| AR | ARGENTINA |
| AM | ARMENIA |
| AW | ARUBA |
| AU | AUSTRALIA |
| AT | AUSTRIA |
| AZ | AZERBAIJAN |
| BS | BAHAMAS |
| BH | BAHRAIN |
| BD | BANGLADESH |
| BB | BARBADOS |
| BY | BELARUS |
| BE | BELGIUM |
| BZ | BELIZE |
| BJ | BENIN |
| BM | BERMUDA |
| BT | BHUTAN |
| BO | BOLIVIA, PLURINATIONAL STATE OF |
| BQ | BONAIRE, SINT EUSTATIUS AND SABA |
| BA | BOSNIA AND HERZEGOVINA |
| BW | BOTSWANA |
| BV | BOUVET ISLAND |
| BR | BRAZIL |
| IO | BRITISH INDIAN OCEAN TERRITORY |
| BN | BRUNEI DARUSSALAM |
| BG | BULGARIA |
| BF | BURKINA FASO |
| BI | BURUNDI |
| KH | CAMBODIA |
| CM | CAMEROON |
| CA | CANADA |
| CV | CAPE VERDE |
| KY | CAYMAN ISLANDS |
| CF | CENTRAL AFRICAN REPUBLIC |
| TD | CHAD |
| CL | CHILE |
| CN | CHINA |
| CX | CHRISTMAS ISLAND |
| CC | COCOS (KEELING) ISLANDS |
| CO | COLOMBIA |
| KM | COMOROS |
| CG | CONGO |
| CD | CONGO, THE DEMOCRATIC REPUBLIC OF THE |
| CK | COOK ISLANDS |
| CR | COSTA RICA |
| CI | CÔTE D'IVOIRE |
| HR | CROATIA |
| CU | CUBA |
| CW | CURAÇAO |
| CY | CYPRUS |
| CZ | CZECH REPUBLIC |
| DK | DENMARK |
| DJ | DJIBOUTI |
| DM | DOMINICA |
| DO | DOMINICAN REPUBLIC |
| EC | ECUADOR |
| EG | EGYPT |
| SV | EL SALVADOR |
| GQ | EQUATORIAL GUINEA |
| ER | ERITREA |
| EE | ESTONIA |
| ET | ETHIOPIA |
| FK | FALKLAND ISLANDS (MALVINAS) |
| FO | FAROE ISLANDS |
| FJ | FIJI |
| FI | FINLAND |
| FR | FRANCE |
| GF | FRENCH GUIANA |
| PF | FRENCH POLYNESIA |
| TF | FRENCH SOUTHERN TERRITORIES |
| GA | GABON |
| GM | GAMBIA |
| GE | GEORGIA |
| DE | GERMANY |
| GH | GHANA |
| GI | GIBRALTAR |
| GR | GREECE |
| GL | GREENLAND |
| GD | GRENADA |
| GP | GUADELOUPE |
| GU | GUAM |
| GT | GUATEMALA |
| GG | GUERNSEY |
| GN | GUINEA |
| GW | GUINEA-BISSAU |
| GY | GUYANA |
| HT | HAITI |
| HM | HEARD ISLAND AND MCDONALD ISLANDS |
| VA | HOLY SEE (VATICAN CITY STATE) |
| HN | HONDURAS |
| HK | HONG KONG |
| HU | HUNGARY |
| IS | ICELAND |
| IN | INDIA |
| ID | INDONESIA |
| IR | IRAN, ISLAMIC REPUBLIC OF |
| IQ | IRAQ |
| IE | IRELAND |
| IM | ISLE OF MAN |
| IL | ISRAEL |
| IT | ITALY |
| JM | JAMAICA |
| JP | JAPAN |
| JE | JERSEY |
| JO | JORDAN |
| KZ | KAZAKHSTAN |
| KE | KENYA |
| KI | KIRIBATI |
| KP | KOREA, DEMOCRATIC PEOPLE'S REPUBLIC OF |
| KR | KOREA, REPUBLIC OF |
| KW | KUWAIT |
| KG | KYRGYZSTAN |
| LA | LAO PEOPLE'S DEMOCRATIC REPUBLIC |
| LV | LATVIA |
| LB | LEBANON |
| LS | LESOTHO |
| LR | LIBERIA |
| LY | LIBYA |
| LI | LIECHTENSTEIN |
| LT | LITHUANIA |
| LU | LUXEMBOURG |
| MO | MACAO |
| MK | MACEDONIA, THE FORMER YUGOSLAV REPUBLIC OF |
| MG | MADAGASCAR |
| MW | MALAWI |
| MY | MALAYSIA |
| MV | MALDIVES |
| ML | MALI |
| MT | MALTA |
| MH | MARSHALL ISLANDS |
| MQ | MARTINIQUE |
| MR | MAURITANIA |
| MU | MAURITIUS |
| YT | MAYOTTE |
| MX | MEXICO |
| FM | MICRONESIA, FEDERATED STATES OF |
| MD | MOLDOVA, REPUBLIC OF |
| MC | MONACO |
| MN | MONGOLIA |
| ME | MONTENEGRO |
| MS | MONTSERRAT |
| MA | MOROCCO |
| MZ | MOZAMBIQUE |
| MM | MYANMAR |
| NA | NAMIBIA |
| NR | NAURU |
| NP | NEPAL |
| NL | NETHERLANDS |
| NC | NEW CALEDONIA |
| NZ | NEW ZEALAND |
| NI | NICARAGUA |
| NE | NIGER |
| NG | NIGERIA |
| NU | NIUE |
| NF | NORFOLK ISLAND |
| MP | NORTHERN MARIANA ISLANDS |
| NO | NORWAY |
| OM | OMAN |
| PK | PAKISTAN |
| PW | PALAU |
| PS | PALESTINE, STATE OF |
| PA | PANAMA |
| PG | PAPUA NEW GUINEA |
| PY | PARAGUAY |
| PE | PERU |
| PH | PHILIPPINES |
| PN | PITCAIRN |
| PL | POLAND |
| PT | PORTUGAL |
| PR | PUERTO RICO |
| QA | QATAR |
| RE | RÉUNION |
| RO | ROMANIA |
| RU | RUSSIAN FEDERATION |
| RW | RWANDA |
| BL | SAINT BARTHÉLEMY |
| SH | SAINT HELENA, ASCENSION AND TRISTAN DA CUNHA |
| KN | SAINT KITTS AND NEVIS |
| LC | SAINT LUCIA |
| MF | SAINT MARTIN (FRENCH PART) |
| PM | SAINT PIERRE AND MIQUELON |
| VC | SAINT VINCENT AND THE GRENADINES |
| WS | SAMOA |
| SM | SAN MARINO |
| ST | SAO TOME AND PRINCIPE |
| SA | SAUDI ARABIA |
| SN | SENEGAL |
| RS | SERBIA |
| SC | SEYCHELLES |
| SL | SIERRA LEONE |
| SG | SINGAPORE |
| SX | SINT MAARTEN (DUTCH PART) |
| SK | SLOVAKIA |
| SI | SLOVENIA |
| SB | SOLOMON ISLANDS |
| SO | SOMALIA |
| ZA | SOUTH AFRICA |
| GS | SOUTH GEORGIA AND THE SOUTH SANDWICH ISLANDS |
| SS | SOUTH SUDAN |
| ES | SPAIN |
| LK | SRI LANKA |
| SD | SUDAN |
| SR | SURINAME |
| SJ | SVALBARD AND JAN MAYEN |
| SZ | SWAZILAND |
| SE | SWEDEN |
| CH | SWITZERLAND |
| SY | SYRIAN ARAB REPUBLIC |
| TW | TAIWAN, PROVINCE OF CHINA |
| TJ | TAJIKISTAN |
| TZ | TANZANIA, UNITED REPUBLIC OF |
| TH | THAILAND |
| TL | TIMOR-LESTE |
| TG | TOGO |
| TK | TOKELAU |
| TO | TONGA |
| TT | TRINIDAD AND TOBAGO |
| TN | TUNISIA |
| TR | TURKEY |
| TM | TURKMENISTAN |
| TC | TURKS AND CAICOS ISLANDS |
| TV | TUVALU |
| UG | UGANDA |
| UA | UKRAINE |
| AE | UNITED ARAB EMIRATES |
| GB | UNITED KINGDOM |
| US | UNITED STATES |
| UM | UNITED STATES MINOR OUTLYING ISLANDS |
| UY | URUGUAY |
| UZ | UZBEKISTAN |
| VU | VANUATU |
| VE | VENEZUELA, BOLIVARIAN REPUBLIC OF |
| VN | VIET NAM |
| VG | VIRGIN ISLANDS, BRITISH |
| VI | VIRGIN ISLANDS, U.S. |
| WF | WALLIS AND FUTUNA |
| EH | WESTERN SAHARA |
| YE | YEMEN |
| ZM | ZAMBIA |
| ZW | ZIMBABWE |

# Footnotes

The National Authority can issue a code.

Stamping involves marking the metal part of the firearm by applying pressure on a mould or matrix, inducing a permanent deformation of the crystalline structure of the material. If someone erases the stamped marking on the surface of the firearm, there can still be a legible trace of the marking in the metal itself. These changes in the physical properties of the material can then be used to restore the markings. Erased stamped markings can be retrieved in about 1/3 of cases. Micro-percussion is a more sophisticated stamping process, also called pin stamping, that allows the marking of uneven surfaces, very hard materials, and plastics. The potential fragility of some parts should be considered when using this method to avoid damage.

# Text boxes

CIFTA00636E01